## Slide 1
By Dyuti Ghosh, Soutrik Acharya, Ratul Chakraborty, Sayan Nandi and Sudeshna Pahari
Obstacle
Avoiding
Bot
BTech 6th Semester Mini Project

## Slide 2
In this Presentation
Here's what we'll cover:
What is an obstacle avoidance bot?
Sensors
Ultrasonic Sensors
Algorithm, Components, Schematic
Practical Demonstration
Observation
Applications

## Slide 3
What is an obstacle avoidance robot?
Obstacle Avoidance is a means of a robot being able to move around in an unknown environment without colliding withsurrounding objects.
(The figure represents a diagramatic representation of the same)

## Slide 4
Introduction to Sensors
A sensor is a device that detects and responds to some type of input from
the physical environment.
The specific input could be light, heat, motion, moisture, pressure.
The output is generally a signal that is converted to human-readable form

## Slide 5
Ultrasonic sensors are sensors that convert ultrasound waves
to electrical signals or vice versa.
The sound beyond human hearing range ( 20,000 Hz ) is known as
ultrasonic.
Introduction to Ultrasonic Sensors

## Slide 6
How does an Ultrasonic Sensor work?
A transmitter that sends out a signal that humans cannot hear
The time it takes to receive the waves back provides them with a very good estimate of the distance.
A receiver that receives the signal after it has bounced off nearby objects
The sensor sends out its signal and determines how long the signal takes to come back.
2 parts of an Ultrasonic Sensor
are:
They emit sound waves and receive back reflected waves.

## Slide 7
The distance has been calculated using
Distance = ½ T x C
(T = Time,
C = the speed of sound=342m/s)
The sensor gives readings of T in µs.
Therefore,
Distance (in cm) = ½ T x 0.0342
While moving forward, if this distance is found to be less than a minimum value, then the car is quickly stopped and reversed.
HC-SR04

## Slide 8
Components
used
We have used 2 non-rechargable batteries. One to power the arduino and hence the ultrasonic sensor. The other was to power the motor driver and hence the motors.
ARDUINO UNO
1
ULTRASONIC SENSOR HC-SR04
2
MOTOR DRIVER L298N
3
2 DC MOTOR WITH WHEELS
4
9V BATTERIES
5

## Slide 9
The Schematic

## Slide 10
The Algorithm
for the Obstacle Avoidance Bot

## Slide 11
The bot drives through freely and moves forward if there are no obstacles in front.

## Slide 12
When obstacle is detected within
30cm to 15cm
it will blink the LED.

## Slide 13
When the obstacle is less than 15cm it will stop. Takes reverse. And then turns right.

## Slide 14
OBSERVATIONS

## Slide 15
Without Obstacle!
This was the observation when there were no obstacle in the bot's way!
Distance
100 cm (fixed)
Time
12.15 seconds (observed)
Speed
8.23 cm/second (calculated)

## Slide 16
With Obstacle!
  Now, the distance was kept fixed at 100 cm.
  Then the obstacles were placed in different
  location in its path.
  The time taken to cover the 100 cm was recorded.
  The speed is then calculated.
  This was then repeated by increasing the number
  of obstacles as 1, 2, 3, 4, and 5.
  Thus 5 such records were noted for each of the 5 cases.

## Slide 17
With Obstacle - CASE 1
No of obstacles = 1
Distance of obstacle from starting point = 50 cm
Distance
100 cm (fixed)
Time
14.55 seconds (observed)
Speed
6.87 cm / second (calculated)

## Slide 18
With Obstacle - CASE 2
No of obstacles = 2
Distance from starting point for
Obstacle 1 => 30 cm II Obstacle 2 => 60 cm
Distance
100 cm (fixed)
Time
17.05 seconds (observed)
Speed
5.87 cm / second (calculated)

## Slide 19
With Obstacle - CASE 3
No of obstacles = 3
Distance from starting point for
Obstacle 1 => 25 cm II Obstacle 2 => 50 cm II Obstacle 3 => 75 cm
Distance
100 cm (fixed)
Time
20.45 seconds (observed)
Speed
4.89 cm / second (calculated)

## Slide 20
With Obstacle - CASE 4
No of obstacles = 4
Distance from starting point for
Obstacle 1 => 20 cm II Obstacle 2 => 40 cm
Obstacle 3 => 60 cm II Obstacle 4 => 80 cm
Distance
100 cm (fixed)
Time
23.85 seconds (observed)
Speed
4.19 cm / second (calculated)

## Slide 21
With Obstacle - CASE 5
No of obstacles = 5
Distance from starting point for
Obstacle 1 => 10 cm II Obstacle 2 => 30 cm
Obstacle 3 => 50 cm II Obstacle 4 => 70 cm II Obstacle 5 => 90 cm
Distance
100 cm (fixed)
Time
28.25 seconds (observed)
Speed
3.54 cm / second (calculated)

## Slide 22
Note.
With each case of increasing obstacles,
    The time taken to cover same distance has increased.
    The speed has thus decreased.

## Slide 23
APPLICATIONS
There are various applications. The exposure to hazards are mitigated to the person who operate the vehicle from a location of relative safety.
Deep
Oceans
Space
Explorations
Fire Exinguisher Car
Military
Engagements

## Slide 24
Team
  Dyuti Ghosh
T91/ECE/184062
  Soutrik Acharya
T91/ECE/184065
  Ratul Chakraborty
T91/ECE/186012
  Sayan Nandi
T91/ECE/186006
  Sudeshna Pahari
T91/ECE/186015
ANY QUESTIONS?